## Slide 1: Catch up on previous topics
Summary and putting together first four classes

## Slide 2: SYSTEM I/O
Uses the SYSCALL command: The SYSCALL can do many different operations.
Each operation is given a number.
The syscall expects to find the operation number in register $v0.
Arguments being sent are in $a0 and maybe $a1.

## Slide 3: Syscall Table
Description | operation code (in $v0) | values passed
Print an integer | 1 | Integer printed is in $a0
Print a string | 4 | Address of a null termintated string in $a0
Read an integer | 5 | Integer returned in $v0
Read a string | 8 | Address of buffer in $a0, max length in $a1
Terminate | 10 | No arguments

## Slide 4: Read/Write Example
.data
p: .asciiz “Input now”
r: .asciiz “answer”
.txt
main: la $a0,p
li $v0,4 #prompt
syscall
li $v0,5 #input
syscall
addi $a0,$v0,100
li $v0,1
syscall
li $v0,10
syscall

## Slide 5: Strings
There are two kinds, ASCII and ASCIIZ
Recall from C++ that strings were implemented as an array of characters with a null (\0=0) terminator.
A variable initialized as .ASCIIZ will have the null terminator (\0) at the end of the string.
.ASCII will not have the null terminator.
The syscall print string expects to see a null.

## Slide 6
.data
hello_msg: .ascii "Hello" # The word "Hello"
.ascii " " # the space.
.ascii "World" # The word "World"
.ascii "\n" # A newline.
.byte 0 # a 0 byte.
IS EQUIVALENT TO:
hello_msg: .asciiz “Hello World\n”

## Slide 7: Various commands
la - load the address of a variable. (very, very different from lw.
li – loads the immediate argument into a register. Because of the instruction format, the value must fit into 16 bits
lui – loads the upper 16 bits of a register with the 16 bits in the immediate field. Sets lower 16 bits to 0
ori – logical or of a register with a 16 bit immediate operand.

## Slide 8: Jump
Much like the b statement for unconditional branch (which means you cannot use b as a variable name), there is an unconditional jump.
Note: b is really a macro command that gets translated into: bgez $0, label
Jump is just: j label.
Branch statements can only branch 215 statements away. Jump can jump to anywhere on the same 226 instruction group. (more later).

## Slide 9: Shift
srl
sra
sll